## Slide 1: PCR Troubleshooting
Virginia Balke
Delaware Technical Community College
CCURI Lab Methods Workshop
Tulsa Community College
July 2015

## Slide 2: Day 1
Thursday, July 9

## Slide 3: Reaction Components
Template – Target DNA
Taq Polymerase
Buffer (2x, 5x, 10x)
Magnesium chloride
dNTPs
Primers – Forward and Reverse
  0.1 to 0.5 μM

## Slide 4: Template
Quantity and Quality
Quantity depends on type
  Plasmid 1 pg to 1 ng
  Genomic 1 ng to 1 μg
Quality depends on source
  Avoid freeze/thaw
  Keep on ice

## Slide 5: Taq Polymerases
Standard
  No 3’ 5’ exonuclease proofreading
  3’ A for Topo TA cloning
  1/1,000 to 1/10,000 error rate
Hot Start
  Modifications that inhibit activity until heating
  Antibodies, covalent modifications, aptamers

## Slide 6: Taq Polymerases
High Fidelity
  3’ 5’ exonuclease proofreading
  Blunt ends
  1/100,000 to 1/1,000,000 error rate
Rapid Cycling
  Steps are shortened to 5 to 10 seconds

## Slide 7: Magnesium Chloride
Cofactor for enzymes
Stabilizes DNA and dNTPs
Increasing MgCl2, increases Tm
Most PCR Master Mixes contain 1.5 mM MgCl2
Can be optimized

## Slide 8: Different Types of Kits
Each component is separate
2x or 10x Master Mixes
Components to increase specificity
Loading dye

## Slide 9: Designing Cycling Conditions
Initial denaturation
  95°C for 2 – 5 minutes
Denaturation
  95°C for 30 seconds
Annealing
  2 – 5 degrees below lowest primer Tm
  30 – 60 seconds
Extension
  72°C
  Time depends on length of amplicon
  1 kb for 1 minute
Repeat 30 – 35 cycles
Final extension at 72°C for 5 – 15 minutes
Hold 4 – 12°C

## Slide 10: Calculating Primer Tm
2°C x (A + T) + 4°C x (G + C)

## Slide 11: Day 2
Friday July 10

## Slide 12: DNA Barcodes for Everyday Life
Reaction mixture
  MgCl2 concentration?
Use of multiple primers
Percentage of NS

## Slide 13: Barcoding at DTCC
Microbiology
  16S rRNA on cultured soil microbes
  Master Mix is prepared by instructor
Biotechnology
  Culture independent analysis of soil microbes
  Insects as part of bat diet project
  Students increasingly learn to do calculations and make own master mix

## Slide 14: Barcoding at DTCC
Research Projects
  Fern Species
  Big Brown Bat diet (primer specificity issues)
  Species confirmation of bats
  Mouse ID

## Slide 15: Mammal Barcoding
Template is mouse genomic DNA
COX primers
  Forward
    TCAACCAACCACAAAGACATTGGCAC Tm = 65
  Reverse
    TAGACTTCTGGGTGGCCAAAGAATCA Tm = 65
Amplicon size 650 bp

## Slide 16: Optimizing Reaction Conditions
Template Concentration
Primer Concentration
MgCl2 Concentration
Temperature Gradient
Negative and Positive Control

## Slide 17: PCR Setup
Three different Taq formulations
  Qiagen HotStarTaq Master Mix
  Qiagen TopTaq Master Mix
  Qiagen TopTaq Polymerase
Three different MgCl2 concentrations
Three different temperatures
20 μL reactions, 2 μL template
1 μL primer mix

## Slide 18: Calculating MgCl2
Master Mixes and Buffers contain 1.5 mM MgCl2
To bring to 2.5 mM – add 1 mM MgCl2
To bring to 4 mM – add 2.5 mM MgCl2

## Slide 19: Cycling Conditions
95°C 5 minutes
35x
  95°C for 1 min
  43, 52, or 58°C 30 sec
  72°C 30sec
72°C 15 minutes
12°C Hold

## Slide 20: Primer Design
18 – 30 bases in length
40 – 60% GC content
Aim for Tm of 55 to 70°C
Tm of pair should be similar
Have C or A at 3’ terminal (they do not wobble)
Avoid runs of 3 or more of the same base
Avoid complementarity between the two primers
Avoid hairpins internally
Avoid self-complementarity

## Slide 21: Primer Design
Design primers for a gene from Sphingobacterium sp. ML3W
Use IDT to analyze primers
  http://www.idtdna.com/calc/analyzer

## Slide 22: Primer Design
As much as possible – make sure that your primer pair does not bind elsewhere in the genome
Use BLAST http://blast.ncbi.nlm.nih.gov/Blast.cgi to check if your primers bind to a unique site in the Sphingobacterium sp. ML3W genome
  BLAST nucleotide
  Align two or more sequences
  Paste your primers into the first box
  Paste the ML3W Accession number: CP009278.1 into the second box